## Slide 1: Combustion of Zero Carbon Fuels MSc Engineering with Finance Mahima Gunewardena
Department of mechanical engineering

## Slide 2: Overview
The Problem
Aims and Objectives
Current Research
Experimental Findings
Economics
Summary
Future works will be highlighted by the icon:

## Slide 3: The Problem
[1] - “Teach About Climate Change With These 24 New York Times Graphs (Published 2019),” The New York Times, 2023. Accessed: Sep. 09, 2023. [Online]. Available: https://www.nytimes.com/2019/02/28/learning/teach-about-climate-change-with-these-24-new-york-times-graphs.html
‌
Global temperatures are increasing due to increasing greenhouse gas emissions

## Slide 4: The Problem
Even the most stringent scenarios would not meet the targets required to prevent irreversible impacts on ecosystems, economies, and societies
[2] “Global Energy Perspective 2022,” McKinsey & Company, Apr. 26, 2022. https://www.mckinsey.com/industries/oil-and-gas/our-insights/global-energy-perspective-2022 (accessed Sep. 10, 2023).
‌

## Slide 5: The Solution
[3] - N. Lash, Tapio Melgin, Agata Mucha-Geppert, and Ole Rolser, “Charting the global energy landscape to 2050: Sustainable fuels,” McKinsey & Company, Jul. 07, 2022. https://www.mckinsey.com/industries/oil-and-gas/our-insights/charting-the-global-energy-landscape-to-2050-sustainable-fuels (accessed Sep. 10, 2023).
‌
Electric Vehicle’s Ideal Target
Mass Adoption Challenges
Alternative Fuels can be used which emit less carbon emissions to help bridge the decarbonization gap

## Slide 6: Aims and Objectives
Fuel Formation
Determine optimal methods for fuel production
Chemical Analysis
Establish fuel blend composition
Combustion Characteristics
Assess combustion cycle's control, reliability, and efficiency
Economic Viability
Evaluate the financial feasibility of fuel production
Research Gap: Combustion Properties of Ammonia / Alcohol Blends

## Slide 7
Ammonia
[5] - A. Valera-Medina, H. Xiao, M Owen-Jones, and P. J. Bowen, “Ammonia for power,” ResearchGate, Nov. 2018. https://www.researchgate.net/publication/328665528_Ammonia_for_power (accessed Sep. 10, 2023).
‌
NH3 has a very high volumetric and energy density – great H2 carrier
  Higher power output with less volume
  Longer travel ranges possible
  Storage and transportation cost reductions

## Slide 8
Combustion Problems:
Low flame speed
High auto-ignition temperature
High heat of vaporization
Narrow flammability limits (16-25 % by volume in air)
Ammonia
Mix with a solvent which itself has great combustion characteristics
Dual Fuel Approach
[5] S. H. Crolius, “Switzerland – Page 2 – Ammonia Energy Association,” Ammoniaenergy.org, 2019. https://www.ammoniaenergy.org/regions/switzerland/page/2/ (accessed Sep. 10, 2023).
‌

## Slide 9: Current Research
[4] - “Mixtures of Ammonia and Organic Solvents as Alternative Fuel for Internal Combustion Engines,” Energy & Fuels, 2019.https://pubs.acs.org/doi/full/10.1021/acs.energyfuels.9b01450?casa_token=2M9RNuwZOzMAAAAA:WDafUJS8a7dVivvubSOOTLHZQmtHPfalpo28g8KCNY2Bcpqdja9KcEfNyB6YodHQd0gdsK7eqWTNICQi (accessed Sep. 10, 2023).
‌
Figure xxx - Conductor-like Screening Model for Real Solvents [4]
The longer the carbon chain the lower the solubility
Carboxylic Acids – Highest Solubility
  Excluded since they don’t exhibit good combustion properties
Mostly Alcohols and Di-alcohols are considered

## Slide 10: Current Research
Lower CO2 emissions as NH3 content increases
[4] - “Mixtures of Ammonia and Organic Solvents as Alternative Fuel for Internal Combustion Engines,” Energy & Fuels, 2019.https://pubs.acs.org/doi/full/10.1021/acs.energyfuels.9b01450?casa_token=2M9RNuwZOzMAAAAA:WDafUJS8a7dVivvubSOOTLHZQmtHPfalpo28g8KCNY2Bcpqdja9KcEfNyB6YodHQd0gdsK7eqWTNICQi (accessed Sep. 10, 2023).
‌
*A5 = 5 wt% NH3
LHV (Lower Heating Value) of NH3 / Solvent Mixtures
  Up to 70% - 50% compared to Gasoline

## Slide 11: Experimental Findings
ID | Item
A | Heating mantle
B | Heating flask with aqueous ammonia
C | Thermometer
D | Stopcock
E | One way valve
F | Rubber tubing
G | Gas washing bottle with sparger and rasching rings
H | Ethanol
I | Column packing
Fuel Mixture Preparation
[6]
Rate of mass transfer
Concentration Gradient
Interfacial Area
Mass transfer coefficient
Increase area = Increase rate
Raschig Rings + Sparger

## Slide 12: Experimental Findings
Chemical Analysis - Calorimetry
Ethanol J/g | Ethanol + NH3 / J/g | Methanol J/g | Methanol + NH3 J/g
25,838 | 27,528 | 15,504 | 16,868
24,373 | 24,929 | 17,508 | 19,344
23,380 | 24,060 | 16,459 | 18,891
24,228 | 24,422 | 18,232 | 18,303
24,218 | 25,207 | 17,759 | 17,589
24,865 | 24,384 | 16,261 | 18,653
The difference between calorific values was used to identify presence of NH3
Ethanol Mixture – 3 wt% NH3 of mixture
Methanol Mixture – 6 wt% NH3 of mixture

## Slide 13: Experimental Findings
Chemical Analysis - Acid Base Titrations
Chart: Volume of Sulfuric Acid / ml
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 42 | 45 | 47 | 50 | 52 | 55 | 60 | 65
 | 8.5 | 8.3 | 8.1 | 7.9 | 7.7 | 7.3 | 7 | 6.5 | 6 | 4.5 | 3.5 | 3 | 2.8 | 2.7 | 2.6 | 2.5 | 2.4
Chart: Volume of Sulfuric Acid / ml
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 42 | 45 | 47 | 50 | 52 | 55 | 60 | 65
dpH / dV | 0.04 | 0.04 | 0.04 | 0.04 | 0.08 | 0.06 | 0.1 | 0.1 | 0.75 | 0.33333 | 0.25 | 0.066667 | 0.05 | 0.033333 | 0.02 | 0.02
[6] A. Cher, “O Level titration TYS questions | Chem Not Cheem,” Chem Not Cheem, Jun. 06, 2020. https://chemnotcheem.com/o-level-acid-base-titration-questions/ (accessed Sep. 11, 2023).
‌
Figure xxx – Methyl Orange colour indication range [6]
Figure xxx – Ethanol Titration Curve
Figure xxx – Ethanol Titration Curve Equivalence Point

## Slide 14: Experimental Findings
Figure xxx – NH3 solubility in solvents [7]
Chart: Temperature / °C
| 0 | 10 | 15 | 20 | 25 | 30 | 35 | 40
Methanol | 0.29321 | 0.23307 | 0.20751 | 0.18087 | 0.15681 | 0.13297 | 0.11471 | 0.098812
Ethanol | 0.18638 | 0.14264 | 0.1226 | 0.10816 | 0.09308 | 0.08166 | 0.071103
The NH3 wt% for both solvents are consistent for both methods
Lower than expected, didn’t reach the solubility limit
~ 8 wt%
~ 13 wt%
Sample | Average Titre / ml | NH3 wt %
Ethanol | 41 | 3.8
Methanol | 62 | 6.3
Measure how long it takes for equilibrium to reach via pH measurements
Investigate how additives could improve the solubility of NH3
  Alkali metal salts have been shown to suppress ammonia vaporization [8]
[8] S. Salentinig, P. Jackson, and M. I. Attalla, “A computational study of the suppression of ammonia volatility in aqueous systems using ionic additives,” Structural Chemistry, vol. 25, no. 1, pp. 159–168, Apr. 2013, doi: https://doi.org/10.1007/s11224-013-0263-8.
‌
[7] - “Table V Solubility of Ammonia in Alcohols*.” Available: https://airgasspecialtyproducts.com/wp-content/uploads/2016/02/Solubility_of_Ammonia_in_Alcohols_.pdf
‌

## Slide 15: Experimental Findings
Ricardo E6 Engine - spark ignition, 600 rpm, naturally aspirated, λ = 1, Compression Ratio = 4.5, Spark Timing = 13 (BTDC), wide open throttle
All parameters were kept constant for samples with the same solvents.
Engine Testing
PURE
PETROL
BLEND

## Slide 16: Experimental Findings
Combustion Characteristic | Pure Ethanol | Ethanol + NH3
Average NIMEP | 7.356 | 7.813
Average GIMEP | 7.469 | 7.916
COV NIMEP | 0.083 | 0.039
COV GIMEP | 0.08 | 0.036
NH3 has provided more power and improved engine efficiency
NH3 has also provided more stable combustion
Engine Testing

## Slide 17: Experimental Findings
Engine Testing
Chart: Numeber of Runs
| Pure Methanol 1 + NH3 | Pure Methanol 2 + NH3 | Pure Methanol 3 + NH3 | Pure Methanol 4 + NH3 | Pure Methanol 3 + NH3
Average NIMEP | 7.758 | 7.666 | 7.565 | 7.491 | 7.292
COV NIMEP | 0.024 | 0.03 | 0.033 | 0.032 | 0.035
Chart: Number of runs
| Pure Methanol 1 | Pure Methanol 2 | Pure Methanol 3 | Pure Methanol 4 | Pure Methanol 5
Average NIMEP | 7.414 | 7.89 | 7.956 | 7.867 | 7.831
COV NIMEP | 0.051 | 0.026 | 0.026 | 0.028 | 0.03
Possible fuel stratification
Molecular Dynamic Simulations and Spectroscopic Techniques (LIF)

## Slide 18: Experimental Findings
1 month
Fuel degradation observed for all samples
A larger visual change in the Methanol / NH3 sample compared to Ethanol / NH3
Degraded samples were not tested, performance losses expected
Isotrope tracing to determine chemical mechanism of degradation under various conditions with GCMS analysis
1 month

## Slide 19: Economics
Chart: 
| Operating Costs | Raw Materials | Utiliites
Cost / L | 0.52183 | 0.46841 | 0.0097599
Figure xxx – Manufacturing cost drivers
Figure xxx – Aspen Simulation Flowsheet
Operating costs are the majority of the costing but are predictable and fairly consistent
Raw Materials costs are highly volatile
Fuel | £ / L
Ethanol / NH3 | 5.79
Petrol | 1.43
Diesel | 1.69

## Slide 20: Economics
Monte Carlo Simulation
Figure xxx – Monte Carlo
Equations Used [8] :
)
Assumptions:
Future returns are normally distributed
Efficient Market Hypothesis
Constant Drift
Constant Variance
[8] “Monte Carlo Simulation: History, How it Works, and 4 Key Steps,” Investopedia, 2023. https://www.investopedia.com/terms/m/montecarlosimulation.asp (accessed Sep. 11, 2023).
‌

## Slide 21: Economics
Figure xxx – Statistical Analysis of Monte Carlo Simulation
Monte Carlo Simulation
[x]“Merton Jump Diffusion Model with Python,” Codearmo.com, 2021. https://www.codearmo.com/python-tutorial/merton-jump-diffusion-model-python (accessed Sep. 12, 2023).
‌
Jump diffusion models could be implemented which allows for better capture of market events
Back testing of Monte Carlo simulations to determine which distributions are appropriate

## Slide 22: Economics
Monte Carlo Simulation
Jump diffusion models could be implemented which allows for better capture of market events
Back testing of Monte Carlo simulations to determine which distributions are appropriate
Figure xxx – Jump Diffusion Model [x]
[x]“Merton Jump Diffusion Model with Python,” Codearmo.com, 2021. https://www.codearmo.com/python-tutorial/merton-jump-diffusion-model-python (accessed Sep. 12, 2023).
‌

## Slide 23: Economics
Figure xxx – Fundamentals of ARIMA
Breaks time series data into patterns and replicates them in the future
4 main patterns: Seasonality, General Trend, Cyclicality and Noise

## Slide 24: Economics
Figure xxx – Ethanol 5-year prediction
The model closely follows historical data and thus can be considered robust
A relative price increase is forecasted for the next 5 years.
Increased demand in the future expected
Investment Opportunity
Time Series Data : Goldman Sachs Chicago Ethanol Index

## Slide 25: Conclusion
As of today, cost of fuel would make it unattractive
Demand increase indicated by Monte Carlo and ARIMA models.
To make the fuel competitive, tax levies, incentives and policy changes would be required
Ammonia-based fuel samples exhibited more power and better combustion stability
A decrease in power in all ammonia-based samples, could indicate fuel stratification
Fuel blends did not reach their solubility limits, difficulty suppressing vaporization
Technical
Economical